## Slide 1: Learning-based Adjustable Beam Number Training Algorithm and Experimental Implementation for Millimeter Wave
Speaker: Ting-Wei Chang
(tony840525@gmail.com)
Advisor: Kai-Ten Feng, Ph.D, Professor
(ktfeng@mail.nctu.edu.tw)
Institute of Communications Engineering
National Chiao Tung University (NCTU) Hsinchu, Taiwan
September 12th, 2019

## Slide 2: Outline
Introduction
System Model
  IEEE 802.11ad/ay Beam Training Frame Structure
  Problem Formulation
Learning-based Adjustable Beam Number Training (LABNT) Algorithm
  Supervised Learning Modeling
  Uniformly Distributed Mutual Information (UDMI) Method
  Reinforcement Learning-based Beam Number Decision
Simulation Results
Experimental Results
Conclusions
References

## Slide 3: Outline
Introduction
System Model
  IEEE 802.11ad/ay Beam Training Frame Structure
  Problem Formulation
Learning-based Adjustable Beam Number Training (LABNT) Algorithm
  Supervised Learning Modeling
  Uniformly Distributed Mutual Information (UDMI) Method
  Reinforcement Learning-based Beam Number Decision
Simulation Results
Experimental Results
Conclusions
References

## Slide 4: Introduction (1/5)
For past few years, abundant applications require extremely high throughput or low latency, e.g., AR/VR and high deﬁnition video [1], [2]
Frequency bands at sub-6 GHz becomes insufﬁcient due to increments of novel applications and mobile devices
  mmWave provides high throughput thanks to its extremely large bandwidth
Although mmWave can provide huge spectrum resource, there are also some disadvantages to be solved
  Severe attenuation by rain or oxygen absorption [3]
  Suffer from much higher path loss than low frequency signal
These will limit the transmission range and power with mmWave system
  Beamforming technique is adopted to overcome high path loss and attenuation due to the enhanced antenna gain [4]
  With beamforming, mmWave signals will become directional and its transmission range will also increase due to higher transmission power [5]
  Therefore, we have to find the optimal beam direction to maximize throughput

## Slide 5: IEEE 802.11ad/ay Beam Training Frame Structure (2/4)
During BTI, the AP will train its optimal transmission beam, so called initiator sector sweep (ISS)
  The AP will beacon sector sweep (SSW) frames from sequential sectors
  In these SSW frames, the receiving user equipment (UE) will obtain the beam (index) ID and signal-to-noise ratio (SNR) of each beam

## Slide 6: References (1/3)
[1] S. Scott-Hayward and E. Garcia-Palacios, “High Deﬁnition Video in IEEE 802.15.3c mm-Wave Wireless Personal Area Networks,” in Proc. IEEE 36th Conference on Local Computer Networks (LCN), pp. 93–100, Oct. 2011.
[2] S. Borkar and H. Pande, “Application of 5G Next Generation Network to Internet of Things,” in Proc. International Conference on Internet of Things and Applications (IOTA), pp. 443–447, Jan. 2016.
[3] R. K. Crone, “Propagation Effects at Millimeter Wavelengths,” in Proc. IEEE Military Communications Conference (MILCOM), vol. 2, pp. 432–437 , Oct. 1985.
[4] W. Roh, J. Seol, J. Park et al., “Millimeter-wave Beamforming as an Enabling Technology for 5G Cellular Communications: Theoretical Feasibility and Prototype Results,” IEEE Communications Magazine, vol. 52, no. 2, pp. 106–113, Feb. 2014.
[5] V. Raghavan, S. Subramanian, J. Cezanne et al., “Directional Beamforming for Millimeter-Wave MIMO Systems,” in Proc. IEEE Global Communications Conference (GLOBECOM), pp. 1–7, Dec. 2015.
[6] T. Nitsche, C. Cordeiro, A. B. Flores et al., “IEEE 802.11ad: Directional 60 GHz Communication for Multi-Gigabit-per- second Wi-Fi,” IEEE Communications Magazine, vol. 52, no. 12, pp. 132–141, Dec. 2014.
[7] Y. Ghasempour, C. R. C. M. da Silva, C. Cordeiro et al., “IEEE 802.11ay: Next-Generation 60 GHz Communication for 100 Gb/s Wi-Fi,” IEEE Communications Magazine, vol. 55, no. 12, pp. 186–192, Dec. 2017.